## Slide 1
Battery Pack E71
07-Apr-2025

## Slide 2: Inputs
CAD
FEM - Example
SDI5-00035091-000.007-EXPORT E71 PHEV2.5 HVB CAD CW13.5.stp
270-PO63__-S1-hv_module______-_-___-__-_____-__-______-_-HV_BM-011-c7344d06___wo_cuves.key
FEM - High pack

## Slide 3: Position
CAD
Use CAD position of the BP,
Move FE-Model by -150mm in X

## Slide 4: MESHING
HOUSING:
Target Element length = 6mm
(The example model was 5.0 mm)
Shells:
Target Element length = 5mm

## Slide 5: MESHING
HOUSING:
Target Element length = 6mm
(The example model was 5.0 mm)
Shells:
Target Element length = 5mm
HOUSING:
3 ribs inside with Element length = 8mm

## Slide 6: MESHING: cells
The Cells with spacers shall be taken from High Pack
Cells in the example – One block
To be shared

## Slide 7: MESHING: Spacer
The MID for the spacer from High Pack

## Slide 8: MESHING: wiring
No CAD for the wires and its plastic covers available! Do not include in the new FE-Model.

## Slide 9: MESHING: electronics
Will not be meshed

## Slide 10: MESHING: END BLOCK
END_BLOCK_SOL
As Hexa mesh (not as Shells as in PAM-CRASH models)

## Slide 11: Bolts - Housing
1. Beams spiders
2. Bolts with pre-tension

## Slide 12: Bolts - Housing
Take the bolts and holes(in the housing) from the example
1. Create skin-shells on the housing
2. Use the skin-shells by housing meshing  due to matching to the solid bolts

## Slide 13: front structure
To be taken from example

## Slide 14: front structure
Bottom cover  perimeters no needed

## Slide 15: front structure
OPTT is used

## Slide 16: Sensors
Take the ACC sensors from the example

## Slide 17: INTERSECTIONS in CAD
Information will follow

## Slide 18: INTERSECTIONS in CAD
Do not mesh the sealing  the cover will be connected by TIED

## Slide 19: INTERSECTIONS in CAD

## Slide 20: Delivery
FE-Model
Deadline: 20.04.2025